Table S1: Summary of test conditions.

| Test type | Static (Algae) and static-renewal (Invertebrate and Fish) |
| --- | --- |
| Test organisms | Algae 3-7 days post-inoculation; C. dubia< 24 hours (hrs) old neonates; Fish 2-6 days swim-up fry |
| Test duration | 72-hrs for algae; 7-days for invertebrate and fish |
| Test replicates | 10 test replicates per treatment for C. dubia; 4 replicates per treatment for fish and algae; plus, controls (negative and positive) |
| Number of Organisms | 10,000 cell/ml for algae; 1 per replicate for C. dubia; 5 per replicate for fish. |
| Laboratory control water | Deionized water supplemented with nutrients for algae; 20% Perrier water and 80% deionized water (hardness 80-100 mg/L CaCO3) plus selenium (5µg/L) and vitamin B12 (12 µg/L) for C. dubia; and moderately hard reconstituted water for fish. |
| Test solution renewal | Daily (Invertebrate and fish tests only) |
| Test temperature | 24 ± 2°C (algae); 25 ± 1°C (invertebrate); 15 ± 1°C (Fish) |
| Feeding | Daily (Invertebrate and Fish tests only) |
| Light intensity | 100 to 600 lux at water surface (invertebrate and fish); 3,600 – 4,400 lux (algae) |
| Photoperiod | 24-hrs light for algae; 16-hrs light/8-hrs dark for invertebrate and fish |
| Test endpoints | Algae: growth; invertebrate: survivaland reproduction; fish: survival and growth |
| Reference toxicant (standard chemical used to calculate the sensitivity of the used organisms) | Algae: Zinc (added as zinc chloride/zinc sulphate) Invertebrate: Sodium chloride Fish: Copper (added as copper chloride) |
| Test Acceptance | Algae: >16-fold increase in number of algal cells, coefficient of variation ≤ 20%; no trend when analyzed using Mann-Kendall test, Invertebrate: >80% control survival in each of the performed test plus applicable reproductive requirements for C. dubia>15 young per surviving control producing three broods ≥60% of controls producing three or more broods, no ephippia present and, Fish: ≥ 90% mean survival; ≥1.5 times average initial dry weight. |

Table S2:General water chemistry, total and dissolved metal concentrations measured in laboratory water, Latte Creek and Halfway Creek collected during winter time and prior to test initiation.

|  | Laboratory Control | Site Control Latte Creek | Site Control Halfway Creek |
| --- | --- | --- | --- |
| Parameter | Lowest Detection Limit | Units | Water | Water | Water |
| Physical Tests (Water) |  |  |  |  |  |
| Conductivity | 2.0 | uS/cm | 290 | 550 | 340 |
| Hardness (as CaCO3) | 0.50 | mg/L | 100 | 390 | 300 |
| pH | 0.10 | pH | 8.3 | 7.8 | 8 |
| Total Dissolved Solids | 13 | mg/L |  | 220 | 205 |
| Total Suspended Solids | 3.0 | mg/L |  | <3.0 | <3.0 |
| Anions and Nutrients (Water) |  |  |  |  |  |
| Alkalinity, Total (as CaCO3) | 1.0 | mg/L | 84 | 92 | 78 |
| Ammonia, Total (as N) | 0.0050 | mg/L |  | 0.858 | 0.799 |
| Sulfate (SO4) | 0.30 | mg/L |  | 163 | 78 |
| Organic / Inorganic Carbon (Water) |  |  |  |  |  |
| Dissolved Organic Carbon | 0.50 | mg/L | <0.50 | 4.8 | 4.3 |
| Total Organic Carbon | 0.50 | mg/L | <0.50 | 5.4 | 6.1 |
| Total Metals (Water) |  |  |  |  |  |
| Aluminum (Al)-Total | 0.0030 | mg/L | <0.0030 | 0.0120 | 0.0112 |
| Antimony (Sb)-Total | 0.00010 | mg/L | 0.00017 | 0.00011 | 0.00053 |
| Arsenic (As)-Total | 0.00010 | mg/L | <0.00010 | 0.00351 | 0.00148 |
| Barium (Ba)-Total | 0.000050 | mg/L | 0.00547 | 0.0296 | 0.0644 |
| Beryllium (Be)-Total | 0.00010 | mg/L | <0.00010 | <0.00010 | <0.00010 |
| Bismuth (Bi)-Total | 0.000050 | mg/L | <0.000050 | <0.000050 | <0.000050 |
| Boron (B)-Total | 0.010 | mg/L | <0.010 | <0.010 | <0.010 |
| Cadmium (Cd)-Total | 0.0000050 | mg/L | <0.0000050 | 0.0000154 | 0.0000118 |
| Calcium (Ca)-Total | 0.050 | mg/L | 40.4 | 74.8 | 49.1 |
| Chromium (Cr)-Total | 0.00010 | mg/L | <0.00010 | 0.00012 | 0.00014 |
| Cobalt (Co)-Total | 0.00010 | mg/L | <0.00010 | <0.00010 | <0.00010 |
| Copper (Cu)-Total | 0.00050 | mg/L | <0.00050 | 0.00123 | 0.00109 |
| Iron (Fe)-Total | 0.030 | mg/L | <0.030 | <0.030 | <0.030 |
| Lead (Pb)-Total | 0.000050 | mg/L | <0.000050 | <0.000050 | <0.000050 |
| Lithium (Li)-Total | 0.0050 | mg/L | <0.0050 | <0.0050 | <0.0050 |
| Magnesium (Mg)-Total | 0.10 | mg/L | 1.10 | 22.4 | 19.8 |
| Manganese (Mn)-Total | 0.00010 | mg/L | 0.00080 | 0.0129 | 0.0064 |
| Molybdenum (Mo)-Total | 0.000050 | mg/L | 0.000223 | 0.000440 | 0.001480 |
| Nickel (Ni)-Total | 0.00050 | mg/L | <0.00050 | 0.00055 | <0.00050 |
| Phosphorus (P)-Total | 0.30 | mg/L | <0.30 | <0.30 | <0.30 |
| Potassium (K)-Total | 2.0 | mg/L | <2.0 | 5.2 | 3.1 |
| Selenium (Se)-Total | 0.000050 | mg/L | 0.00293 | 0.000169 | 0.000169 |
| Silicon (Si)-Total | 0.10 | mg/L | 1.17 | 5.84 | 6.11 |
| Silver (Ag)-Total | 0.000010 | mg/L | <0.000010 | <0.000010 | <0.000010 |
| Sodium (Na)-Total | 2.0 | mg/L | 2.5 | 7.7 | 5.3 |
| Strontium (Sr)-Total | 0.00020 | mg/L | 0.171 | 0.509 | 0.501 |
| Thallium (Tl)-Total | 0.00010 | mg/L | <0.00010 | <0.00010 | <0.00010 |
| Tin (Sn)-Total | 0.00010 | mg/L | 0.00014 | <0.00010 | <0.00010 |
| Titanium (Ti)-Total | 0.010 | mg/L | <0.010 | <0.010 | <0.010 |
| Uranium (U)-Total | 0.000010 | mg/L | 0.000572 | 0.0245 | 0.0741 |
| Vanadium (V)-Total | 0.00050 | mg/L | <0.00050 | <0.00050 | <0.00050 |
| Zinc (Zn)-Total | 0.0030 | mg/L | <0.0030 | 0.0034 | 0.0033 |
| Dissolved Metals (Water) |  |  |  |  |  |
| Aluminum (Al)-Dissolved | 0.0010 | mg/L | <0.0010 | 0.0109 | 0.0100 |
| Antimony (Sb)-Dissolved | 0.00010 | mg/L | 0.00015 | <0.00010 | 0.00045 |
| Arsenic (As)-Dissolved | 0.00010 | mg/L | <0.00010 | 0.00347 | 0.00140 |
| Barium (Ba)-Dissolved | 0.000050 | mg/L | 0.00665 | 0.0324 | 0.0683 |
| Beryllium (Be)-Dissolved | 0.00010 | mg/L | <0.00010 | <0.00010 | <0.00010 |
| Bismuth (Bi)-Dissolved | 0.000050 | mg/L | <0.000050 | <0.000050 | <0.000050 |
| Boron (B)-Dissolved | 0.010 | mg/L | <0.010 | <0.010 | <0.010 |
| Cadmium (Cd)-Dissolved | 0.0000050 | mg/L | 0.0000056 | 0.0000108 | 0.0000089 |
| Calcium (Ca)-Dissolved | 0.050 | mg/L | 46.3 | 79.6 | 50.7 |
| Chromium (Cr)-Dissolved | 0.00010 | mg/L | <0.00010 | <0.00010 | 0.00012 |
| Cobalt (Co)-Dissolved | 0.00010 | mg/L | <0.00010 | <0.00010 | <0.00010 |
| Copper (Cu)-Dissolved | 0.00020 | mg/L | <0.00020 | 0.00115 | 0.00097 |
| Iron (Fe)-Dissolved | 0.030 | mg/L | <0.030 | <0.030 | <0.030 |
| Lead (Pb)-Dissolved | 0.000050 | mg/L | 0.000090 | <0.000050 | <0.000050 |
| Lithium (Li)-Dissolved | 0.0010 | mg/L | <0.0010 | 0.0029 | 0.0016 |
| Magnesium (Mg)-Dissolved | 0.10 | mg/L | 1.24 | 24.0 | 21.7 |
| Manganese (Mn)-Dissolved | 0.00010 | mg/L | <0.00010 | 0.00144 | 0.00129 |
| Molybdenum (Mo)-Dissolved | 0.000050 | mg/L | 0.000228 | 0.000421 | 0.001400 |
| Nickel (Ni)-Dissolved | 0.00050 | mg/L | <0.00050 | <0.00050 | <0.00050 |
| Phosphorus (P)-Dissolved | 0.30 | mg/L | <0.30 | <0.30 | <0.30 |
| Potassium (K)-Dissolved | 2.0 | mg/L | <2.0 | 5.9 | 3.3 |
| Selenium (Se)-Dissolved | 0.000050 | mg/L | 0.00309 | 0.000090 | 0.000148 |
| Silicon (Si)-Dissolved | 0.050 | mg/L | 1.32 | 5.63 | 5.72 |
| Silver (Ag)-Dissolved | 0.000010 | mg/L | <0.000010 | <0.000010 | <0.000010 |
| Sodium (Na)-Dissolved | 2.0 | mg/L | 3.0 | 8.3 | 5.8 |
| Strontium (Sr)-Dissolved | 0.00020 | mg/L | 0.188 | 0.539 | 0.522 |
| Thallium (Tl)-Dissolved | 0.000010 | mg/L | <0.000010 | <0.000010 | <0.000010 |
| Tin (Sn)-Dissolved | 0.00010 | mg/L | 0.00015 | <0.00010 | <0.00010 |
| Titanium (Ti)-Dissolved | 0.010 | mg/L | <0.010 | <0.010 | <0.010 |
| Uranium (U)-Dissolved | 0.000010 | mg/L | 0.000653 | 0.0240 | 0.0721 |
| Vanadium (V)-Dissolved | 0.00050 | mg/L | <0.00050 | <0.00050 | <0.00050 |
| Zinc (Zn)-Dissolved | 0.0010 | mg/L | <0.0010 | 0.0012 | 0.0015 |
| Notes: < less than; N - Nitrogen |  |  |  |  |  |

Table S3:General water chemistry, total and dissolved metal concentrations measured in laboratory water, Latte Creek and Halfway Creek collected during summer time and prior to test initiation.

|  | Laboratory Control | Site Control Latte Creek | Site Control HalfwayCreek |
| --- | --- | --- | --- |
| Parameters | Lowest Detection Limit | Units | Water | Water | Water |
| Physical Tests (Water) |  |  |  |  |  |
| Conductivity | 2.0 | uS/cm | 215 | 308 | 195 |
| Hardness (as CaCO3) | 0.50 | mg/L | 100 | 151 | 88.6 |
| pH | 0.10 | pH | 8.43 | 7.90 | 7.82 |
| Total Suspended Solids | 3.0 | mg/L |  | <3.0 | <3.0 |
| Total Dissolved Solids | 13 | mg/L |  | 225 | 148 |
| Anions and Nutrients (Water) |  |  |  |  |  |
| Alkalinity, Total (as CaCO3) | 1.0 | mg/L | 75 | 86.0 | 66.2 |
| Ammonia, Total (as N) | 0.0050 | mg/L | <0.50 | <0.0050 | <0.0050 |
| Sulfate (SO4) | 0.30 | mg/L | <0.50 | 71.4 | 29.0 |
| Organic / Inorganic Carbon (Water) |  |  |  |  |  |
| Dissolved Organic Carbon | 0.50 | mg/L |  | 8.22 | 9.44 |
| Total Organic Carbon | 0.50 | mg/L |  | 8.68 | 9.55 |
| Total Metals (Water) |  |  |  |  |  |
| Aluminum (Al)-Total | 0.0030 | mg/L | <0.0030 | 0.0772 | 0.101 |
| Antimony (Sb)-Total | 0.00010 | mg/L | <0.00010 | 0.00015 | 0.00049 |
| Arsenic (As)-Total | 0.00010 | mg/L | <0.00010 | 0.00067 | 0.00111 |
| Barium (Ba)-Total | 0.00010 | mg/L | 0.00016 | 0.0420 | 0.0369 |
| Beryllium (Be)-Total | 0.00010 | mg/L | <0.00010 | <0.00010 | <0.00010 |
| Bismuth (Bi)-Total | 0.000050 | mg/L | <0.000050 | <0.000050 | <0.000050 |
| Boron (B)-Total | 0.010 | mg/L | 0.031 | <0.010 | <0.010 |
| Cadmium (Cd)-Total | 0.0000050 | mg/L | <0.0000050 | 0.0000073 | 0.0000056 |
| Calcium (Ca)-Total | 0.050 | mg/L | 0.792 | 39.5 | 23.5 |
| Chromium (Cr)-Total | 0.00010 | mg/L | <0.00010 | 0.00027 | 0.00045 |
| Cobalt (Co)-Total | 0.00010 | mg/L | 0.00020 | <0.00010 | <0.00010 |
| Copper (Cu)-Total | 0.00050 | mg/L | 0.0143 | 0.00157 | 0.00159 |
| Iron (Fe)-Total | 0.030 | mg/L | <0.030 | 0.051 | 0.074 |
| Lead (Pb)-Total | 0.000050 | mg/L | 0.000283 | <0.000050 | <0.000050 |
| Lithium (Li)-Total | 0.0050 | mg/L | <0.0050 | <0.0050 | <0.0050 |
| Magnesium (Mg)-Total | 0.10 | mg/L | 1.60 | 13.5 | 8.64 |
| Manganese (Mn)-Total | 0.00010 | mg/L | 0.0641 | 0.00459 | 0.00275 |
| Molybdenum (Mo)-Total | 0.000050 | mg/L | 0.00177 | 0.000162 | 0.00128 |
| Nickel (Ni)-Total | 0.00050 | mg/L | <0.00050 | 0.00056 | 0.00071 |
| Phosphorus (P)-Total | 0.30 | mg/L | <0.30 | <0.30 | <0.30 |
| Potassium (K)-Total | 2.0 | mg/L | <2.0 | 2.3 | <2.0 |
| Selenium (Se)-Total | 0.000050 | mg/L | <0.000050 | 0.000123 | 0.000070 |
| Silicon (Si)-Total | 0.10 | mg/L | <0.10 | 5.73 | 5.62 |
| Silver (Ag)-Total | 0.000010 | mg/L | <0.000010 | <0.000010 | <0.000010 |
| Sodium (Na)-Total | 2.0 | mg/L | 6.8 | 3.2 | 2.7 |
| Strontium (Sr)-Total | 0.00020 | mg/L | <0.00020 | 0.326 | 0.270 |
| Thallium (Tl)-Total | 0.00010 | mg/L | <0.00010 | <0.00010 | <0.00010 |
| Tin (Sn)-Total | 0.00010 | mg/L | <0.00010 | <0.00010 | <0.00010 |
| Titanium (Ti)-Total | 0.010 | mg/L | <0.010 | <0.010 | <0.010 |
| Uranium (U)-Total | 0.000010 | mg/L | <0.000010 | 0.00825 | 0.0228 |
| Vanadium (V)-Total | 0.00050 | mg/L | <0.00050 | <0.00050 | <0.00050 |
| Zinc (Zn)-Total | 0.0030 | mg/L | 0.0123 | <0.0030 | <0.0030 |
| Dissolved Metals (Water) |  |  |  |  |  |
| Dissolved Metals Filtration Location |  | - | LAB | LAB | LAB |
| Aluminum (Al)-Dissolved | 0.0010 | mg/L | <0.0010 | 0.0692 | 0.0793 |
| Antimony (Sb)-Dissolved | 0.00010 | mg/L | <0.00010 | 0.00013 | 0.00042 |
| Arsenic (As)-Dissolved | 0.00010 | mg/L | <0.00010 | 0.00066 | 0.00101 |
| Barium (Ba)-Dissolved | 0.00010 | mg/L | 0.00014 | 0.0435 | 0.0387 |
| Beryllium (Be)-Dissolved | 0.00010 | mg/L | <0.00010 | <0.00010 | <0.00010 |
| Bismuth (Bi)-Dissolved | 0.000050 | mg/L | <0.000050 | <0.000050 | <0.000050 |
| Boron (B)-Dissolved | 0.010 | mg/L | 0.031 | <0.010 | <0.010 |
| Cadmium (Cd)-Dissolved | 0.0000050 | mg/L | 0.0000075 | 0.0000060 | 0.0000061 |
| Calcium (Ca)-Dissolved | 0.050 | mg/L | 0.798 | 39.1 | 22.5 |
| Chromium (Cr)-Dissolved | 0.00010 | mg/L | <0.00010 | 0.00033 | 0.00038 |
| Cobalt (Co)-Dissolved | 0.00010 | mg/L | 0.00020 | <0.00010 | <0.00010 |
| Copper (Cu)-Dissolved | 0.00020 | mg/L | 0.0127 | 0.00148 | 0.00141 |
| Iron (Fe)-Dissolved | 0.030 | mg/L | <0.030 | 0.041 | 0.053 |
| Lead (Pb)-Dissolved | 0.000050 | mg/L | 0.000164 | <0.000050 | <0.000050 |
| Lithium (Li)-Dissolved | 0.0010 | mg/L | <0.0010 | 0.0020 | 0.0012 |
| Magnesium (Mg)-Dissolved | 0.10 | mg/L | 1.56 | 12.9 | 7.84 |
| Manganese (Mn)-Dissolved | 0.00010 | mg/L | 0.0690 | 0.00414 | 0.00234 |
| Molybdenum (Mo)-Dissolved | 0.000050 | mg/L | 0.00176 | 0.000189 | 0.00120 |
| Nickel (Ni)-Dissolved | 0.00050 | mg/L | <0.00050 | 0.00051 | 0.00062 |
| Phosphorus (P)-Dissolved | 0.30 | mg/L | <0.30 | <0.30 | <0.30 |
| Potassium (K)-Dissolved | 2.0 | mg/L | <2.0 | 2.4 | <2.0 |
| Selenium (Se)-Dissolved | 0.000050 | mg/L | <0.000050 | 0.000100 | 0.000069 |
| Silicon (Si)-Dissolved | 0.050 | mg/L | <0.050 | 5.45 | 5.40 |
| Silver (Ag)-Dissolved | 0.000010 | mg/L | <0.000010 | <0.000010 | <0.000010 |
| Sodium (Na)-Dissolved | 2.0 | mg/L | 7.1 | 3.2 | 2.6 |
| Strontium (Sr)-Dissolved | 0.00020 | mg/L | 0.00047 | 0.328 | 0.259 |
| Thallium (Tl)-Dissolved | 0.000010 | mg/L | <0.000010 | <0.000010 | <0.000010 |
| Tin (Sn)-Dissolved | 0.00010 | mg/L | <0.00010 | <0.00010 | <0.00010 |
| Titanium (Ti)-Dissolved | 0.010 | mg/L | <0.010 | <0.010 | <0.010 |
| Uranium (U)-Dissolved | 0.000010 | mg/L | <0.000010 | 0.00900 | 0.0228 |
| Vanadium (V)-Dissolved | 0.00050 | mg/L | <0.00050 | <0.00050 | <0.00050 |
| Zinc (Zn)-Dissolved | 0.0010 | mg/L | 0.0122 | <0.0010 | <0.0010 |
| Notes: < less than; N - Nitrogen |  |  |  |  |  |

Table S4: Water quality parameters for Ceriodaphnia dubia, rainbow trout and Pseudokirchneriella subcapitata exposed to a – Metal Mixtures inLatte Creek and Halfway Creek water collected at two different times of the year.

| Ceriodaphnia dubia | Metal Mixtures |
| --- | --- |
| Latte Creek Water | Water Quality Parameters (Mean ± SD) |
| Treatments | Temperature | DO | pH | Conductivity |
|  | (°C) | (mg/L) | (pH units) | (µS/cm) |
| Summer 2018 - August |
| Lab. Control | 25 ± 0.5 | 7.7 ± 0.4 | 7.9 ± 0.2 | 209 ± 5.7 |
| Site Control | 25 ± 0.5 | 7.8 ± 0.4 | 7.7 ± 0.2 | 257 ± 3.2 |
| Low | 25 ± 0.5 | 7.8 ± 0.4 | 7.7 ± 0.2 | 257 ± 2.5 |
| Moderate | 25 ± 0.5 | 7.8 ± 0.4 | 7.6 ± 0.2 | 258 ± 2.3 |
| High | 25 ± 0.5 | 7.8 ± 0.5 | 7.6 ± 0.2 | 258 ± 2.4 |
| Winter 2018 - March |  |  |  |  |
| Lab. Control | 24 ± 0.5 | 7.8 ± 0.3 | 8.1 ± 0.1 | 221 ± 3.4 |
| Site Control | 24 ± 0.5 | 7.8 ± 0.3 | 8.0 ± 0.4 | 588 ± 6.6 |
| Low | 24 ± 0.5 | 7.8 ± 0.3 | 8.0 ± 0.4 | 594 ± 5.4 |
| Moderate | 24 ± 0.5 | 7.8 ± 0.3 | 8.0 ± 0.4 | 595 ± 6.7 |
| High | 24 ± 0.5 | 7.8 ± 0.3 | 8.1 ± 0.4 | 593 ± 5.4 |
| Halfway Creek Water |
| Summer 2018 - August |  |  |  |  |
| Lab Control | 25 ± 0.5 | 7.8 ± 0.4 | 8.0 ± 0.2 | 210 ± 6.5 |
| Un-amended | 25 ± 0.5 | 7.8 ± 0.4 | 7.7 ± 0.2 | 168 ± 2.0 |
| Low | 25 ± 0.5 | 7.8 ± 0.4 | 7.6 ± 0.2 | 168 ± 1.6 |
| Moderate | 25 ± 0.5 | 7.8 ± 0.4 | 7.6 ± 0.2 | 169 ± 1.7 |
| High | 25 ± 0.5 | 7.8 ± 0.4 | 7.5 ± 0.1 | 169 ± 1.9 |
| Winter 2018 - March |  |  |  |  |
| Lab. Control | 24 ± 0.5 | 7.7 ± 0.3 | 8.0 ± 0.1 | 221 ± 3.4 |
| Site Control | 24 ± 0.5 | 7.8 ± 0.3 | 8.1 ± 0.2 | 397 ± 62.7 |
| Low | 24 ± 0.5 | 7.8 ± 0.3 | 8.1 ± 0.3 | 397 ± 62.7 |
| Moderate | 24 ± 0.5 | 7.8 ± 0.3 | 8.1 ± 0.3 | 398 ± 63.2 |
| High | 24 ± 0.5 | 7.8 ± 0.3 | 8.1 ± 0.2 | 398 ± 59.2 |
| Rainbow trout Latte Creek Water | Water Quality Parameters(Mean ± SD) |
| Treatments | Temperature | DO | pH | Conductivity |
|  | (°C) | (mg/L) | (pH units) | (µS/cm) |
| Summer 2018 - August |  |  |  |  |
| Lab. Control | 15 ± 0.1 | 9.0 ± 1.5 | 7.4 ± 0.2 | 345 ± 1.5 |
| Site Control | 15 ± 0.3 | 9.0 ± 1.4 | 7.3 ± 0.2 | 254 ± 4.6 |
| Low | 15 ± 0.3 | 9.0 ± 1.4 | 7.3 ± 0.2 | 256 ± 4.3 |
| Moderate | 15 ± 0.3 | 8.9 ± 1.6 | 7.3 ± 0.2 | 256 ± 4.7 |
| High | 15 ± 0.3 | 9.0 ± 1.5 | 7.3 ± 0.2 | 255 ± 3.5 |
| Winter 2018 - March |  |  |  |  |
| Lab Control | 14 ± 0.4 | 9.6 ± 1.0 | 8.0 ± 0.2 | 329 ± 3.8 |
| Un-amended | 14 ± 0.4 | 9.6 ± 1.0 | 8.0 ± 0.2 | 584 ± 5.6 |
| Low | 14 ± 0.4 | 9.5 ± 0.8 | 8.0 ± 0.2 | 583 ± 5.3 |
| Moderate | 15 ± 0.4 | 9.5 ± 0.7 | 8.0 ± 0.2 | 584 ± 4.1 |
| High | 15 ± 0.4 | 9.5 ± 0.7 | 8.0 ± 0.2 | 585 ± 7.5 |
| Halfway Creek Water |
| Summer 2018 - August |  |  |  |  |
| Lab. Control | 15 ± 0.1 | 8.9 ± 1.4 | 7.4 ± 0.3 | 345 ± 2.1 |
| Site Control | 15 ± 0.3 | 8.9 ± 1.4 | 7.2 ± 0.2 | 167 ± 3.5 |
| Low | 15 ± 0.3 | 9.0 ± 1.4 | 7.2 ± 0.2 | 167 ± 2.7 |
| Moderate | 15 ± 0.3 | 9.0 ± 1.4 | 7.2 ± 0.2 | 168 ± 3.7 |
| High | 15 ± 0.3 | 9.0 ± 1.4 | 7.2 ± 0.2 | 169 ± 3.1 |
| Winter 2018 - March |  |  |  |  |
| Lab. Control | 14 ± 0.4 | 9.6 ± 0.9 | 8.0 ± 0.2 | 329 ± 3.8 |
| Site Control | 14 ± 0.4 | 9.6 ± 0.9 | 8.0 ± 0.3 | 412 ± 2.7 |
| Low | 14 ± 0.4 | 9.6 ± 0.8 | 8.0 ± 0.3 | 423 ± 33.2 |
| Moderate | 14 ± 0.4 | 9.6 ± 0.8 | 8.0 ± 0.3 | 413 ± 4.2 |
| High | 14 ± 0.4 | 9.5 ± 1.0 | 8.0 ± 0.3 | 409 ± 8.3 |
| Psuedokirchneriella subcapitata Latte Creek Water |  |
|  | Water Quality Parameters (Mean ± SD) |
| Treatments | Temperature | pH |
|  | (°C) | (pH units) |
| Summer 2018 - August |  |  |
| Lab. Control | 23 | 6.9 |
| Site Control | 23 | 7.8 |
| Low | 23 | 7.8 |
| Moderate | 23 | 7.7 |
| High | 23 | 7.7 |
| Winter 2018 - March |  |  |
| Lab. Control | 24 | 7 |
| Site Control | 24 | 7.8 |
| Low | 24 | 8 |
| Moderate | 24 | 8 |
| High | 24 | 7.9 |
| Halfway Creek Water |  |
| Summer 2018 - August |  |  |
| Lab. Control | 23 | 6.9 |
| Site Control | 23 | 7.6 |
| Low | 23 | 7.6 |
| Moderate | 23 | 7.5 |
| High | 23 | 7.5 |
| Winter 2018 - March |  |  |
| Lab. Control | 24 | 7 |
| Site Control | 24 | 7.7 |
| Low | 24 | 7.9 |
| Moderate | 24 | 7.9 |
| High | 24 | 7.9 |

Table S5: Water quality parameters for Ceriodaphnia dubia, rainbow trout and Pseudokirchneriella subcapitata exposed to a – Metal Mixtures + Nutrients inLatte Creek and Halfway Creek water collected at two different times of the year.

| Ceriodaphnia dubia Latte Creek Water | Metal Mixtures + Nutrients Water Quality Parameters (Mean ± SD) |
| --- | --- |
|  | Temperature (°C) | DO (mg/L) | pH (pH units) | Conductivity (µS/cm) |
| Summer 2018 - August |  |  |  |  |
| Lab. Control | 25 ± 0.4 | 7.8 ± 0.3 | 7.8 ± 0.1 | 219 ± 1.3 |
| Site Control | 25 ± 0.5 | 7.6 ± 0.4 | 7.7 ± 0.1 | 321 ± 3.3 |
| Low | 25 ± 0.7 | 7.6 ± 0.4 | 7.8 ± 0.1 | 775 ± 3.9 |
| Moderate | 25 ± 0.7 | 7.6 ± 0.5 | 7.8 ± 0.1 | 778 ± 2.6 |
| High | 25 ± 0.6 | 7.6 ± 0.4 | 7.8 ± 0.1 | 787 ± 6.2 |
| Winter 2018 - March |  |  |  |  |
| Lab. Control | 24 ± 0.5 | 7.8 ± 0.3 | 8.0 ± 0.2 | 221 ± 3.6 |
| Site Control | 24 ± 0.4 | 7.8 ± 0.3 | 8.0 ± 0.4 | 587 ± 6.9 |
| Low | 24 ± 0.5 | 7.8 ± 0.3 | 8.1 ± 0.3 | 1103 ± 33.4 |
| Moderate | 24 ± 0.5 | 7.8 ± 0.3 | 8.2 ± 0.1 | 1103 ± 16.4 |
| High | 24 ± 0.5 | 7.8 ± 0.3 | 8.3 ± 0.1 | 1106 ± 18.0 |
| Halfway Creek Water |  |  |  |  |
| Summer 2018 - August |  |  |  |  |
| Lab. Control | 25 ± 0.4 | 7.8 ± 0.3 | 7.8 ± 0.1 | 219 ± 1.3 |
| Site Control | 25 ± 0.5 | 7.7 ± 0.4 | 7.5 ± 0.1 | 201 ± 2.6 |
| Low | 25 ± 0.7 | 7.6 ± 0.5 | 7.7 ± 0.1 | 746 ± 9.2 |
| Moderate | 25 ± 0.7 | 7.6 ± 0.4 | 7.7 ± 0.1 | 751 ± 6.9 |
| High | 25 ± 0.6 | 7.6 ± 0.4 | 7.7 ± 0.1 | 685 ± 5.2 |
| Winter 2018 - March |  |  |  |  |
| Lab. Control | 24 ± 0.5 | 7.7 ± 0.3 | 8.0 ± 0.1 | 220 ± 3.4 |
| Site Control | 24 ± 0.5 | 7.8 ± 0.3 | 8.1 ± 0.2 | 397 ± 62.7 |
| Low | 24 ± 0.5 | 7.8 ± 0.3 | 8.2 ± 0.2 | 891 ± 158.4 |
| Moderate | 24 ± 0.5 | 7.8 ± 0.3 | 8.3 ± 0.1 | 907 ± 161.9 |
| High | 24 ± 0.5 | 7.7 ± 0.3 | 8.3 ± 0.1 | 911 ± 162.2 |
| Rainbow trout Latte Creek Water | Water Quality Parameters (Mean ± SD) |
|  | Temperature (°C) | DO (mg/L) | pH (pH units) | Conductivity (µS/cm) |
| Summer 2018 - August |  |  |  |  |
| Lab. Control | 15 ± 0.2 | 9.4 ± 1.1 | 8.1 ± 0.2 | 358 ± 4.9 |
| Site Control | 15 ± 0.0 | 9.2 ± 0.9 | 8.1 ± 0.3 | 322 ± 6.0 |
| Low | 15 ± 0.0 | 9.2 ± 1.0 | 8.1 ± 0.2 | 786 ± 8.1 |
| Moderate | 15 ± 0.1 | 9.2 ± 1.2 | 8.1 ± 0.2 | 785 ± 8.8 |
| High | 15 ± 0.0 | 9.1 ± 1.3 | 8.2 ± 0.3 | 791 ± 8.9 |
| Winter 2018 - March |  |  |  |  |
| Lab Control | 14 ± 0.4 | 9.6 ± 0.9 | 8.0 ± 0.2 | 328 ± 3.8 |
| Un-amended | 14 ± 0.4 | 9.7 ± 0.8 | 8.0 ± 0.4 | 584 ± 5.6 |
| Low | 15 ± 0.4 | 9.4 ± 1.2 | 8.3 ± 0.2 | 1094 ± 9.9 |
| Moderate | 15 ± 0.4 | 9.5 ± 0.9 | 8.3 ± 0.2 | 1099 ± 12.3 |
| High | 15 ± 0.4 | 9.5 ± 1.0 | 8.3 ± 0.2 | 1108 ± 34.4 |
| Halfway Creek water |  |
| Summer 2018 - August |  |  |  |  |
| Lab. Control | 15 ± 0.2 | 9.4 ± 1.1 | 8.1 ± 0.2 | 359 ± 6.7 |
| Site Control | 15 ± 0.1 | 9.0 ± 1.4 | 8.0 ± 0.2 | 201 ± 9.4 |
| Low | 15 ± 0.0 | 9.1 ± 1.2 | 8.0 ± 0.2 | 760 ± 6.5 |
| Moderate | 15 ± 0.1 | 9.2 ± 1.1 | 8.0 ± 0.2 | 754 ± 7.9 |
| High | 15 ± 0.0 | 9.2 ± 1.1 | 8.0 ± 0.2 | 688 ± 7.9 |
| Winter 2018 - March |  |  |  |  |
| Lab. Control | 14 ± 0.4 | 9.6 ± 0.9 | 8.0 ± 0.2 | 329 ± 3.9 |
| Site Control | 14 ± 0.4 | 9.6 ± 0.9 | 8.0 ± 0.3 | 414 ± 6.1 |
| Low | 14 ± 0.4 | 9.6 ± 0.6 | 8.2 ± 0.2 | 955 ± 8.6 |
| Moderate | 14 ± 0.4 | 9.6 ± 0.7 | 8.2 ± 0.2 | 953 ± 7.2 |
| High | 14 ± 0.4 | 9.6 ± 0.7 | 8.3 ± 0.2 | 956 ± 6.9 |
| Psuedokirchneriella subcapitata Latte Creek Water | Water Quality Parameters (Mean ± SD) |
|  | Temperature (°C) | pH (pH units) |
| Summer 2018 - August |  |  |
| Lab. Control | 24 | 7.0 |
| Site Control | 23 | 8.1 |
| Low | 23 | 8.1 |
| Moderate | 23 | 8.1 |
| High | 23 | 8.1 |
| Winter 2018 - March |  |  |
| Lab. Control | 24 | 7.0 |
| Site Control | 24 | 7.8 |
| Low | 24 | 8.3 |
| Moderate | 24 | 8.3 |
| High | 24 | 8.3 |
| Halfway Creek Water |  |
| Summer 2018 - August |  |  |
| Lab. Control | 24 | 7.0 |
| Site Control | 23 | 8.0 |
| Low | 23 | 8.0 |
| Moderate | 23 | 8.0 |
| High | 23 | 8.0 |
| Winter 2018 - March |  |  |
| Lab. Control | 24 | 7.0 |
| Site Control | 24 | 7.7 |
| Low | 24 | 8.3 |
| Moderate | 24 | 8.3 |
| High | 24 | 8.3 |

Notes:SD – Standard Deviation

Table S6: Water quality parameters for Ceriodaphnia dubia, rainbow trout and Pseudokirchneriella subcapitata exposed to a – Metal Mixtures + Nutrients + TDS inLatte Creek and Halfway Creek waters collected in summer.

| Ceriodaphnia dubia | c) Metal Mixtures + Nutrients + TDS |
| --- | --- |
| Latte Creek Water | Water Quality Parameters (Mean ± SD) |
| Treatments | Temperature | DO | pH | Conductivity |
|  | (°C) | (mg/L) | (pH units) | (µS/cm) |
| Summer 2018 - August |
| Lab. Control | 25 ± 0.4 | 7.8 ± 0.3 | 7.8 ± 0.1 | 219 ± 1.3 |
| Site Control | 25 ± 0.5 | 7.6 ± 0.4 | 7.7 ± 0.1 | 321 ± 3.3 |
| Low | 25 ± 0.6 | 7.5 ± 0.5 | 7.8 ± 0.1 | 1122 ± 7.2 |
| Moderate | 25 ± 0.6 | 7.6 ± 0.4 | 7.8 ± 0.1 | 1559 ± 10.3 |
| High | 25 ± 0.6 | 7.6 ± 0.4 | 7.8 ± 0.1 | 1904 ± 10.9 |
| Halfway Creek Water |
| Summer 2018 - August |
| Lab Control | 25 ± 0.4 | 7.8 ± 0.4 | 7.8 ± 0.1 | 219 ± 1.3 |
| Un-amended | 25 ± 0.5 | 7.7 ± 0.4 | 7.5 ± 0.1 | 201 ± 2.6 |
| Low | 25 ± 0.6 | 7.7 ± 0.4 | 7.6 ± 0.1 | 1090 ± 8.0 |
| Moderate | 25 ± 0.6 | 7.7 ± 0.4 | 7.6 ± 0.1 | 1403 ± 9.5 |
| High | 25 ± 0.5 | 7.6 ± 0.4 | 7.6 ± 0.1 | 1835 ± 12.5 |
| Rainbow trout Latte Creek Water | Water Quality Parameters (Mean ± SD) |
| Treatments | Temperature | DO | pH | Conductivity |
|  | (°C) | (mg/L) | (pH units) | (µS/cm) |
| Summer 2018 - August |
| Lab. Control | 15 ± 0.2 | 9.4 ± 1.1 | 8.1 ± 0.2 | 359 ± 6.7 |
| Site Control | 15 ± 0.0 | 9.2 ± 0.9 | 8.1 ± 0.3 | 322 ± 6.0 |
| Low | 15 ± 0.1 | 9.2 ± 1.0 | 8.1 ± 0.2 | 1145 ± 10.7 |
| Moderate | 15 ± 0.1 | 9.2 ± 1.0 | 8.1 ± 0.2 | 1579 ± 16.1 |
| High | 15 ± 0.3 | 9.3 ± 1.0 | 8.1 ± 0.3 | 1934 ± 16.4 |
| Halfway Creek water |
| Summer 2018 - August |
| Lab. Control | 15 ± 0.3 | 9.5 ± 1.0 | 8.1 ± 0.2 | 359 ± 6.7 |
| Site Control | 15 ± 0.1 | 9.0 ± 1.4 | 8.0 ± 0.2 | 201 ± 9.4 |
| Low | 15 ± 0.0 | 9.1 ± 1.1 | 8.0 ± 0.2 | 1110 ± 12.7 |
| Moderate | 15 ± 0.0 | 9.2 ± 0.9 | 8.0 ± 0.2 | 1422 ± 9.4 |
| High | 15 ± 0.0 | 9.1 ± 1.2 | 7.9 ± 0.2 | 1859 ± 9.9 |
| Psuedokirchneriella subcapitata Latte Creek Water | Water Quality Parameters (Mean ± SD) |
| Treatments | Temperature | pH |
|  | (°C) | (pH units) |
| Summer 2018 - August |  |  |
| Lab. Control | 24 | 7 |
| Site Control | 23 | 8.1 |
| Low | 23 | 8.1 |
| Moderate | 23 | 8.1 |
| High | 23 | 8 |
| Halfway Creek Water |  |
| Lab. Control | 24 | 7 |
| Site Control | 23 | 8 |
| Low | 23 | 7.9 |
| Moderate | 23 | 7.9 |
| High | 23 | 7.9 |

Notes: TDS -Total Dissolved Solids; SD -Standard Deviation

Table S7: Measured metal, nutrients,  total dissolved solids and  hardness concentrations for rainbow trout, Ceriodaphnia dubia, and Pseudokirchneriella subcapitata tests using spiked Latte Creek and Halfway Creek water collected at two different times of the year.  Data represents mean (± standard deviation [SD]).

| Latte Creek: a - Metal Mixtures |
| --- |
| Season | Treatments | Rainbow Trout |
| Summer 2018 |  | Arsenic (ug/L) | Chromium (ug/L) | Copper (ug/L) | Uranium (ug/L) | Zinc (ug/L) | Ammonia (mg/L) | Sulphate (mg/L) | TDS (mg/L) | Hardness (as CaCO3) (mg/L) |
|  | Low | 3.08 ± 0.65 | 1.7 ± 0.03 | 4.54 ± 0.29 | 35.00 ± 1.98 | 5.85 ± 0.35 | N/A | N/A | N/A | 117.5 ± 3.54 |
|  | Moderate | 6.12 ± 0.62 | 1.68 ± 0.09 | 4.58 ± 0.24 | 92.15 ± 3.32 | 9.60 ± 0.99 |  |  |  | 119.5 ± 6.36 |
|  | High | 8.92 ± 0.68 | 1.67 ± 0.03 | 4.49 ± 0.30 | 99.80 ± 7.35 | 15.45 ± 2.19 |  |  |  | 117.0 ± 2.83 |
| Winter 2018 |  |  |  |  |  |  |  |  |  |  |
|  | Low | 5.07 ± 0.68 | 1.63 ± 0.12 | 4.61 ± 0.47 | 56.1 ± 3.39 | 4.85 ± 0.07 | N/A | N/A | N/A | 314.0 ± 7.1 |
|  | Moderate | 8.70 ± 0.42 | 1.62 ± 0.01 | 4.68 ± 0.60 | 113.50 ± 4.95 | 8.95 ± 1.06 |  |  |  | 315 ± 9.9 |
|  | High | 11.60 ± 0.42 | 1.63 ± 0.04 | 4.59 ± 0.84 | 129.00 ± 4.24 | 16.55 ± 1.91 |  |  |  | 313 ± 11.3 |
| Latte Creek: b - Mixture + Nutrients |
| Season | Treatments | Rainbow Trout |
| Summer 2018 |  | Arsenic (ug/L) | Chromium (ug/L) | Copper (ug/L) | Uranium (ug/L) | Zinc (ug/L) | Ammonia (mg/L) | Sulphate (mg/L) | TDS (mg/L) | Hardness (as CaCO3) (mg/L) |
|  | Low | 3.10 ± 0.71 | 1.68 ± 0.00 | 4.29 ± 0.09 | 37.35 ± 1.91 | 4.90 ± 0.85 | 2.61 ± 0.89 | 331 ± 11.31 | N/A | 416.5 ± 7.78 |
|  | Moderate | 6.18 ± 0.96 | 1.73 ± 0.07 | 4.40 ± 0.00 | 92.60 ± 2.83 | 7.10 ± 0.57 | 2.48 ± 0.72 | 336 ± 4.24 |  | 423.0 ± 15.56 |
|  | High | 8.69 ± 1.86 | 1.65 ± 0.15 | 4.02 ± 0.35 | 103.00 ± 1.41 | 11.95 ± 0.64 | 2.74 ± 0.75 | 330 ± 20.51 |  | 422.0 ± 35.36 |
| Winter 2018 | Low | 5.11 ± 0.68 | 1.64 ± 0.15 | 4.62 ± 0.17 | 56.90 ± 0.99 | 5.40 ± 0.71 | 2.27 ± 0.47 | 468 ± 9.90 | N/A | 632.5 ± 30.4 |
|  | Moderate | 8.06 ± 0.73 | 2.18 ± 1.05 | 4.08 ± 0.53 | 110.00 ± 2.83 | 8.30 ± 0.14 | 2.24 ± 0.49 | 471 ± 13.44 |  | 602.5 ± 48.8 |
|  | High | 11.35 ± 0.92 | 1.56 ± 0.19 | 4.46 ± 0.35 | 127.5 ± 0.71 | 15.85 ± 0.07 | 2.20 ± 0.48 | 473 ± 13.44 |  | 628.5 ± 4.9 |
| Latte Creek: c - Mixture + Nutrients + TDS |
| Season | Treatments | Rainbow Trout |
| Summer 2018 |  | Arsenic (ug/L) | Chromium (ug/L) | Copper (ug/L) | Uranium (ug/L) | Zinc (ug/L) | Ammonia (mg/L) | Sulphate (mg/L) | TDS (mg/L) | Hardness (as CaCO3) (mg/L) |
|  | Low | 3.21 ± 0.98 | 1.75 ± 0.18 | 4.51 ± 0.29 | 39.65 ± 1.48 | 4.50 ± 1.13 | 2.72 ± 1.04 | 314 ± 0.71 | 943 ± 21.21 | 561.00 ± 18.38 |
|  | Moderate | 6.34 ± 1.03 | 1.74 ± 0.14 | 4.44 ± 0.14 | 91.9 ± 3.11 | 7.15 ± 0.78 | 2.60 ± 0.93 | 342 ± 12.73 | 1440 ± 42.43 | 767.50 ± 31.82 |
|  | High | 9.04 ± 1.33 | 1.68 ± 0.09 | 4.20 ± 0.06 | 110.00 ± 2.83 | 12.9 ± 0.42 | 2.72 ± 1.12 | 329 ± 10.61 | 1790 ± 70.71 | 931.50 ± 16.26 |
| Halfway Creek: a - Metal Mixtures |
| Season | Treatments | Rainbow Trout |
| Summer 2018 |  | Arsenic (ug/L) | Chromium (ug/L) | Copper (ug/L) | Uranium (ug/L) | Zinc (ug/L) | Ammonia (mg/L) | Sulphate (mg/L) | TDS (mg/L) | Hardness (as CaCO3) (mg/L) |
|  | Low | 3.48 ± 0.63 | 1.93 ± 0.00 | 4.92 ± 0.16 | 45.20 ± 1.98 | 5.80 ± 0.28 | N/A | N/A | N/A | 76.5 ± 0.57 |
|  | Moderate | 6.51 ± 0.65 | 1.89 ± 0.03 | 4.90 ± 0.06 | 95.75 ± 7.42 | 12.8 ± 5.37 |  |  |  | 76.65 ± 0.50 |
|  | High | 9.44 ± 0.71 | 1.84 ± 0.01 | 4.78 ± 0.18 | 107.00 ± 5.66 | 16.95 ± 0.92 |  |  |  | 76.2 ± 0.71 |
| Winter 2018 |  |  |  |  |  |  |  |  |  |  |
|  | Low | 3.10 ± 0.39 | 1.66 ± 0.06 | 5.96 ± 0.55 | 104.50 ± 3.54 | 5.95 ± 0.21 | N/A | N/A | N/A | 219 ± 9.9 |
|  | Moderate | 6.53 ± 0.26 | 1.64 ± 0.11 | 4.78 ± 1.06 | 164.5 ± 7.78 | 9.80 ± 1.98 |  |  |  | 224.0 ± 18.4 |
|  | High | 9.91 ± 0.13 | 1.72 ± 0.06 | 4.85 ± 0.65 | 181.00 ± 8.49 | 19.35 ± 2.62 |  |  |  | 217.5 ± 20.5 |
| Halfway Creek: b - Metal Mixtures + Nutrients |
| Season | Treatments | Rainbow Trout |
| Summer 2018 |  | Arsenic (ug/L) | Chromium (ug/L) | Copper (ug/L) | Uranium (ug/L) | Zinc (ug/L) | Ammonia (mg/L) | Sulphate (mg/L) | TDS (mg/L) | Hardness (as CaCO3) (mg/L) |
|  | Low | 3.58 ± 0.96 | 1.78 ± 0.07 | 4.53 ± 0.10 | 53.20 ± 1.13 | 4.40 ± 1.13 | 2.71 ± 0.86 | 329 ± 12.02 | N/A | 412.5 ± 23.33 |
|  | Moderate | 6.59 ± 1.15 | 1.68 ± 0.00 | 4.59 ± 0.23 | 109.5 ± 2.12 | 7.40 ± 0.71 | 2.35 ± 0.60 | 328 ± 12.73 |  | 404.0 ± 22.63 |
|  | High | 8.31 ± 1.12 | 1.59 ± 0.08 | 4.17 ± 0.27 | 106.00 ± 1.41 | 11.50 ± 0.42 | 2.38 ± 1.04 | 284 ± 10.61 |  | 365.50 ± 21.92 |
| Winter 2018 |  | Arsenic (ug/L) | Chromium (ug/L) | Copper (ug/L) | Uranium (ug/L) | Zinc (ug/L) | Ammonia (mg/L) | Sulphate (mg/L) | TDS (mg/L) | Hardness (as CaCO3) (mg/L) |
|  | Low | 3.17 ± 0.62 | 1.65 ± 0.11 | 4.60 ± 0.16 | 102.5 ± 2.12 | 6.05 ± 0.21 | 2.22 ± 0.48 | 386 ± 12.73 | N/A | 542.5 ± 2.1 |
|  | Moderate | 6.67 ± 0.73 | 1.67 ± 0.04 | 4.45 ± 0.18 | 162.5 ± 0.71 | 9.45 ± 0.64 | 2.19 ± 0.55 | 384 ± 4.95 |  | 546.5 ± 13.4 |
|  | High | 9.38 ± 0.86 | 1.58 ± 0.21 | 4.42 ± 0.10 | 178.5 ± 7.78 | 17.5 ± 0.85 | 2.35 ± 0.43 | 382 ± 5.66 |  | 543.0 ± 12.7 |
| Halfway Creek: c - Metal Mixtures + Nutrients+TDS |
| Season | Treatments | Rainbow Trout |
| Summer 2018 |  | Arsenic (ug/L) | Chromium (ug/L) | Copper (ug/L) | Uranium (ug/L) | Zinc (ug/L) | Ammonia (mg/L) | Sulphate (mg/L) | TDS (mg/L) | Hardness (as CaCO3) (mg/L) |
|  | Low | 3.55 ± 0.83 | 1.79 ± 0.06 | 4.39 ± 0.12 | 54.2 ± 1.84 | 4.25 ± 1.20 | 2.59 ± 1.05 | 336 ± 11.31 | 883 ± 25.46 | 551.50 ± 12.02 |
|  | Moderate | 6.47 ± 0.91 | 1.64 ± 0.11 | 4.40 ± 0.04 | 104.5 ± 0.71 | 7.25 ± 1.20 | 2.65 ± 1.05 | 328 ± 17.68 | 1270 ± 98.99 | 689.00 ± 8.49 |
|  | High | 9.46 ± 0.77 | 1.78 ± 0.11 | 4.32 ± 0.07 | 118.50 ± 4.95 | 15.15 ± 2.62 | 2.63 ± 0.98 | 326 ± 20.51 | 1725 ± 49.5 | 889.50 ± 12.02 |

Notes: Data for invertebrate and fish represent  the calculated mean (±standard deviation) from samples collected at test initiation, halfway and termination (n = 3); For algae, samples for metal determinations were collected at test initatio (n = 1); Gray highlighted cells represent concentrations exceeding applicable water qualty guideliens  (Canadian Council of Ministers of the Environment ([CCME] 1999); Chromium values were screened against the chromium (VI) guideline of 1 ug/L;TDS - Total Disoolved Solids; N/A  - not available